## Slide 1: Exp 8 and 9
Decoder and Encoder

## Slide 2: Encoders and Decoders
Encoders and Decoders are Combinational, MSI (Medium-Scale Integration) Circuits.
Binary code of N digits can be used to store 2N distinct elements of coded information.
This is what encoders and decoders are used for.
Encoders convert 2N lines of input into a code of N bit and
Decoders decode the N bits into 2N lines.

## Slide 3: 2 to 4 Line Decoder
In the 2 to 4 line decoder, there is a total of three inputs, i.e., A0, and A1 and E and four outputs, i.e., Y0, Y1, Y2, and Y3.
For each combination of inputs, when the enable 'E' is set to 1, one of these four outputs will be 1.
Truth Table

## Slide 4: 2 to 4 Line Decoder
The logical expression of the term Y0, Y1, Y2, and Y3 is as follows:

## Slide 5: 2 to 4 Line Decoder: Code
module decoder(a,b,c,d,e,f,E);
input a,b,E;
output c,d,e,f;
assign c = E&a&b;
assign d = E&a&(~b);
assign e = E&(~a)&b;
assign f = E&(~a)&(~b);
endmodule
module testbench;
reg a, b, E;
wire c,d,e,f;
decoder obj(a,b,c,d,e,f,E);
initial begin
$display("Inputs | Outputs");
$display("E a b | c d e f");
$monitor("%b %b %b | %b %b %b %b",E,a,b,c,d,e,f);
E=0 ; a=0; b=0;
#5 E=1; a=0; b=0;
#5 E=1; a=0; b=1;
#5 E=1; a=1; b=0;
#5 E=1; a=1; b=1;
#5 $finish;
end
endmodule

## Slide 6: Decoders (3 to 8 line decoder)
A decoder does the opposite job of an encoder. It is a combinational circuit that converts n lines of input into 2n lines of output.
Let’s take an example of 3-to-8 line decoder.
Truth Table
X | Y | Z | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 7: Decoders
Implementation –
D0 is high when X = 0, Y = 0 and Z = 0. Hence,
i.e. D0 = X’ Y’ Z’
Similarly,
D1 = X’ Y’ Z
D2 = X’ Y Z’
D3 = X’ Y Z
D4 = X Y’ Z’
D5 = X Y’ Z
D6 = X Y Z’
D7 = X Y Z

## Slide 8: Encoder
An encoder is a combinational circuit that converts binary information in the form of a 2N input lines into N output lines, which represent N bit code for the input.
For simple encoders, it is assumed that only one input line is active at a time.
4 to 2 Encoder
  Let 4 to 2 Encoder has four inputs Y3, Y2, Y1 & Y0 and two outputs A1 & A0.
  The block diagram of 4 to 2 Encoder is shown in the following figure.

## Slide 9: Encoder (4x2)
At any time, only one of these 4 inputs can be ‘1’ in order to get the respective binary code at the output.
The Truth table of 4 to 2 encoder is shown below.
From Truth table, we can write the Boolean functions for each output as

## Slide 10: Encoder (4x2)
module encoder(a,b,c,d,p,q);
input a,b,c,d;
output p,q;
assign p = a | b;
assign q = a | c;
endmodule
module test;
reg a, b, c, d;
wire p,q;
encoder obj(a,b,c,d,p,q);
initial begin
$display("Inputs | Outputs");
$display("A B C D | P Q");
$monitor("%b %b %b %b | %b %b",a,b,c,d,p,q);
a=0; b=0; c=0; d=1;
#5 a=0; b=0; c=1; d=0;
#5 a=0; b=1; c=0; d=0;
#5 a=1; b=0; c=0; d=0;
end
endmodule

## Slide 11: Encoder (8x3)
Truth Table –
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
As seen from the truth table, the output is 000 when D0 is active; 001 when D1 is active; 010 when D2 is active and so on.
As an example, let’s consider Octal to Binary encoder. As shown in the following figure, an octal-to-binary encoder takes 8 input lines and generates 3 output lines.

## Slide 12: Encoder
Implementation – From the truth table, the output line Z is active when the input octal digit is 1, 3, 5 or 7.
Similarly, Y is 1 when input octal digit is 2, 3, 6 or 7 and X is 1 for input octal digits 4, 5, 6 or 7.
Hence, the Boolean functions would be:
  X = D4 + D5 + D6 + D7
  Y = D2 +D3 + D6 + D7
  Z = D1 + D3 + D5 + D7

## Slide 13: Encoder

## Slide 14: Applications of Encoders and Decoders
Some of the significant applications are –
Speed Control of modern motors.
Night vision cameras
Metal detectors
encoder circuit has applications in Robotic vehicles
Automation system – especially the home automation system.
Automatic Monitoring systems has different types of encoder circuits.
Encoder circuit has utilized in encrypted communications system.